## Slide 1
PLASTECH MANUFACTURING CO.
Manufacturing Plant
Operational Performance
A Root-Cause Analysis of Downtime, Quality & Cost Across the Plant Floor
Prepared for: Plant Operations Leadership & Interview Panel Data Period: January 2018 - March 2026 | 3,000 Production Batch Records Presented by: Data Analyst, Business Intelligence Track

## Slide 2
What We'll
Cover Today
From a production log to a plant-wide action plan.
01
The Business Problem
Why the plant floor manager commissioned this study
02
Data & Method
3,000 records, 20 machines, 8+ years - how we approached it
03
Five Investigations
Assets, quality, shifts, environment, cost - tested against the data
04
Beyond the Brief
Translating findings into rupees, benchmarks & risk
05
Recommendations
A phased roadmap the plant can act on immediately
02

## Slide 3
THE BUSINESS PROBLEM
Tight Margins, Despite Hitting Production Targets
The Plant Operations & Floor Manager commissioned this study with a specific worry: daily output targets are being met, but unpredictable asset failures, excessive rework time, and material waste spikes are quietly eating into margins. The brief was not “work harder” - it was “show me, with evidence, where the money is actually leaking.”
Which shifts or machines really suffer from lower efficiency?
Are scrap and rework tied to a specific cause we can fix?
Is our shop-floor climate control worth the investment?
How do we get to an optimal, defensible cost-per-unit?
“
We are meeting our baseline daily production targets, but we are noticing unacceptably tight margins due to unpredictable asset failures, excessive rework times, and material waste spikes.
Chief Floor & Production Manager
Business Requirement Document, v1.0
This deck answers that brief with evidence -not opinion.
03

## Slide 4
PROJECT SCOPE
Four Questions the Business Needed Answered
01
Asset Reliability
Which machines fail most, and does pouring in more maintenance hours actually help?
02
Quality Assurance
Which product types and lines are driving defects, scrap and failed QC checks?
03
Environmental Control
Do shop-floor temperature and humidity swings really move the needle on quality?
04
Resource & Cost
Is labour over-allocated, and what is really inflating overhead per unit?
04

## Slide 5
DATA & METHOD
One Clean Source of Truth - No Estimates, No Gaps
The dataset is the plant's own operational log: one row per production batch, capturing machine, shift and product type, alongside output, quality, cost, environmental and downtime figures. After cleaning, there were zero missing values in any field used in this analysis - every number in this deck is drawn from the full record set, not a sample.
3,000
Production batch
records
8+ yrs
Jan 2018 --Mar 2026
coverage
20
Machines
tracked
3
Shifts -Day,
Swing, Night
5
Product lines
in scope
TOOLCHAIN
Python (pandas) —-cleaning & exploratory analysis
Statistical correlation testing across 6 hypotheses
Power BI - interactive executive dashboard
DATA DICTIONARY SNAPSHOT
Down time Hours
Critical KPI - unplanned stops
Scrap Rate
Wasted material at setup
Rework Hours
Hidden labour cost
Quality Checks Failed
QA gate rejections
Avg. Temp / Humidity
Climate tolerance check
Maintenance Hours
Proactive vs. reactive care
05

## Slide 6
EXECUTIVE SUMMARY
The Headline Finding: It's Not One Fire - It's Many Small Ones
Every major lever we normally blame for plant losses -temperature, humidity, headcount, maintenance hours, shift timing, product mix - was tested against the data. None of them meaningfully explains our downtime, defects or scrap. Losses are spread evenly across the operation, with one exception: a small group of machines that consistently underperform the fleet.
375,113
Units Produced
across 8-year review period
3.64%
Overall Defect Rate
13,655 total defects logged
12.2%
Downtime-to-Production
4,613 hrs lost of 37,733 run
7,522 hrs
Maintenance Invested
with no measurable downtime cut
4 Machines
Flagged High-Risk
IDs 6, 9, 11 & 18
06

## Slide 7
INVESTIGATION 01 -ASSET RELIABILITY
Five Machines Are Losing More Time Than the Rest of the Fleet
Chart: Downtime / Production Hours (%)
| M6 | M11 | M9 | M7 | M12 | M18 | M1 | M5 | M3 | M13 | M8 | M4 | M10 | M17 | M14 | M20 | M19 | M16 | M15 | M2
Downtime / Production Ratio (%) | 13.99 | 13.52 | 13.37 | 13.05 | 13 | 12.49 | 12.41 | 12.41 | 12.4 | 12.33 | 12.24 | 12.21 | 12.18 | 11.66 | 11.64 | 11.56 | 11.41 | 11.39 | 11.3 | 10.69
FLEET AVERAGE
12.2%
of active production time lost to unplanned downtime, fleet-wide.
THE FIVE OUTLIERS
Machines 6, 11, 9, 7 & 12 each lose 13.0-14.0% of running time - a real, addressable gap above the fleet norm.
This is a spread, not a single outlier - which is why the fix has to be targeted engineering inspection, not a blanket policy change.
07

## Slide 8
INVESTIGATION 01 (CONT.) -THE MAINTENANCE PARADOX
More Maintenance Hours Are Not Buying Less Downtime
Chart: Maintenance Hours Received (bucketed)
| 0–1 hrs | 1–2 hrs | 2–3 hrs | 3–4 hrs | 4–5 hrs
Avg. Downtime Hours per Batch | 1.58 | 1.47 | 1.54 | 1.54 | 1.55
CORRELATION
- 0.004
Maintenance Hours vs. Down Time Hours -effectively zero relationship.
THE STORY HERE
Average downtime stays flat at roughly 1.5 hours whether a machine received 1 hour or 5 hours of maintenance. This doesn't mean maintenance is worthless -it means it's being applied on a fixed calendar rather than in response to a machine's actual condition, so the hours aren't landing where they're needed.
08

## Slide 9
INVESTIGATION 02 -QUALITY & SCRAP
Defects Are a Plant-Wide Pattern -Not One Product's Problem
Chart: 
| Automotive | Appliances | Textiles | Furniture | Electronics
Total Defects | 2921 | 2766 | 2722 | 2646 | 2600
Quality Checks Failed | 645 | 611 | 622 | 565 | 565
DEFECT RATE BAND
3.54% - 3.77%
across all five product lines -too narrow a gap to call any single line the culprit.
SCRAP RATE SPREAD
2.98%-3.12% by product, 2.99%-3.09% by shift. Rework hours also show almost no link to labour pay tier (r = 0.02) -we are not overpaying premium shifts to fix mistakes; rework itself is the cost to target.
09

## Slide 10
INVESTIGATION 03 -SHIFT & STAFFING
Night Shift Isn't the Problem -and Neither Is More Headcount
OUTPUT & DEFECT RATE BY SHIFT
Chart: 
| Day | Night | Swing
Avg. Units Produced / Batch | 124.4 | 124 | 126.6
Swing shift actually edges out Day and Night on both output and defect rate -the long-held “night shift underperforms” assumption isn't supported.
PRODUCTION PER HOUR BY OPERATOR COUNT
Chart: 
| 1 Operator | 2 Operators | 3 Operators | 4 Operators
Units / Hour | 17.32 | 16.76 | 18.02 | 17.5
Correlation between Operator Count and Units Produced: 0.007. Output per hour does not climb with headcount -pointing to a bottleneck in machine speed or material supply, not staffing.
Business read:
Some lines may be over-staffed relative to what they can actually produce -a near-term headcount review is worth more than a shift-schedule overhaul.
10

## Slide 11
INVESTIGATION 04 -ENVIRONMENTAL CONTROL
The Climate-Control Hypothesis Doesn't Hold Up
Temp.
Humidity
Defects
QC Failed
Downtime
Scrap
Temperature
1.00
0.01
0.01
0.01
0.02
0.02
Humidity
0.01
1.00
0.00
0.02
0.05
0.03
Defects
0.01
0.00
1.00
-0.03
0.03
0.00
QC Failed
0.01
0.02
-0.03
1.00
-0.01
0.02
Downtime
0.02
0.05
0.03
-0.01
1.00
0.02
All values between -0.03 and 0.05 -statistically indistinguishable from no relationship.
VERDICT
Hypothesis: Disproven
Temperature and humidity, within the ranges recorded on our floor, are not driving defect or breakdown patterns. That's a cost-saving finding: tighter climate control is not the lever to pull for quality or downtime -and it frees up that budget for the machine-level fixes that actually move the needle.
11

## Slide 12
BEYOND THE BRIEF -ADDED ANALYSIS
Translating the Floor Data Into a Language Leadership Trades In: Money
SHOP-FLOOR HEALTH vs. WORLD-CLASS BENCHMARK
Reframing two of our own KPIs the way lean-manufacturing / TPM programs benchmark plants worldwide.
Chart: 
| Availability | Quality Rate
Plastech (Actual) | 89.1 | 96.4
World-Class Benchmark | 90 | 99
Availability (89.1%) is within reach of world-class. The real gap is Quality Rate -96.4% vs. a 99% benchmark -which is where scrap and rework live.
HIDDEN COST OF VARIABILITY
A cost-of-poor-quality (COPQ) estimate -what downtime, defects and rework are worth in rupees, not just percentages.
₹18.6 Lakh
estimated recoverable value across the review period, at current downtime, scrap and rework levels.
Lost output value from unplanned downtime
₹13.83 L
Material cost tied up in defective units
₹4.12 L
Rework labour cost
₹0.68 L
This is a floor, not a ceiling -it excludes second-order costs like expedited freight, customer credits, or overtime to catch up after a breakdown.
12

## Slide 13
DELIVERABLE -AT-RISK ASSET DIRECTORY
Four Machines, One Priority List for Engineering
Priority | Machine ID | Downtime Ratio | Defect Rate | Avg. Maint. Hrs | QC Failures
1 | Machine 6 | 14% | 4.11% | 2.65 | 129
2 | Machine 9 | 13% | 4.36% | 2.54 | 123
3 | Machine 18 | 12% | 4.52% | 2.75 | 133
4 | Machine 11 | 14% | 4.04% | 2.48 | 171
Machine 11 is a close fourth and worth including in the same inspection cycle. All four run maintenance hours in line with the fleet average -confirming the issue is asset condition, not lack of attention.
13

## Slide 14
RECOMMENDATIONS
A Phased Roadmap -Not a Single Silver Bullet
IMMEDIATE
0-3 Months
Send Machines 6, 9, 11 & 18 for urgent engineering inspection
Audit the maintenance schedule; shift from fixed-interval to condition-based servicing on the 4 at-risk machines first
NEAR-TERM
3-6 Months
Review staffing line-by-line against actual throughput; reallocate headcount from over-staffed to constrained lines
Investigate rework drivers directly -operator training, calibration, material quality -not labour cost tier
ONGOING
Continuous
Do not prioritize climate-control spend as a quality/downtime fix -the evidence doesn't support it
Build a rolling machine-health scorecard; re-run this analysis quarterly to track the at-risk list
14

## Slide 15
THE DELIVERABLE
A Live Dashboard Behind Every Slide
Every chart in this deck is also a live, filterable view in the Power BI dashboard delivered alongside this report -sliced by Machine ID, Shift, Product Type and Month, so plant leadership can self-serve the same answers going forward.
Machine Metrics page -downtime ratio & QC failures by asset
Quality & Cost page -defects, rework, energy vs. temperature
Operational Overview -KPIs, trend, shift & product mix
Thank You
Happy to walk through any metric live, or open the dashboard for a filtered drill-down on request.
15